Experiment No: 05
Experiment Name: Implementation of BPSK and QPSK in MATLAB
Objectives:
1. To simulate BPSK and QPSK modulation schemes in MATLAB using sine carriers for given bit sequences.
2. To visualize time-domain characteristics of input bits, carrier waves, and modulated signals using subplot comparisons.
3. To analyze trade-offs between bandwidth efficiency (QPSK) and phase noise resilience (BPSK) through waveform inspection.
Theory:
#### BPSK (Binary Phase Shift Keying)
Mathematical Representation:
The BPSK signal for the k-th bit is defined as:
s_k(t) = left lbrace stack { A sin(2 %pi f_c t) ~~ "bit 1" # - A sin(2 %pi f_c t) ~~ "bit 0" } right none
where A is amplitude, fc is carrier frequency, and t∈[kTb,(k+1)Tb). This corresponds to phase shifts of 0∘ (logic 1) and 180∘ (logic 0).
- Constellation Diagram:
  BPSK has two constellation points on the real axis at (+A,0) and (−A,0), separated by 2A. The Euclidean distance dmin=2A provides noise immunity.
- Spectral Characteristics:
  The power spectral density (PSD) is given by:

          S_BPSK(f) = {A^2 T_b} over 2 left[ left( {sin(%pi (f - f_c) T_b)} over {%pi (f - f_c) T_b} right)^2 + left( {sin(%pi (f + f_c) T_b)} over {%pi (f + f_c) T_b} right)^2 right]

#### QPSK (Quadrature Phase Shift Keying)
- Signal Decomposition:
  QPSK can be expressed in quadrature form:
    s(t) = I(t) cos(2 %pi f_c t) - Q(t) sin(2 %pi f_c t)
where I(t) and Q(t) are in-phase and quadrature baseband signals mapped as:
Dibit	I	Q
00	+A	+A
01	−A	+A
11	−A	−A
10	+A	−A

- Phase Encoding:
  The code implements offset QPSK due to the sin⁡(2πfct+ϕ) formulation. Phase transitions occur every Ts=2Tb​ seconds, with 90∘ jumps minimizing envelope fluctuations.
- Synchronization:
  BPSK suffers from 180∘ phase ambiguity, requiring differential encoding. QPSK has 90∘ ambiguity, complicating carrier recovery.
Pulse Shaping:
Rectangular pulses (as used in the code) cause high sidelobes. Raised-cosine filtering is typically applied to limit bandwidth.

Discussion:

The implementation of BPSK and QPSK modulation schemes was conducted in MATLAB using sine wave carriers. For BPSK modulation, the input bit sequence [1, 0, 0, 1, 1, 0, 1, 0, 1] was processed, where a phase shift of 0° (sin⁡(2πfct)) was assigned to bit 1, and 180° (−sin⁡(2πfct)) to bit 0. For QPSK, the bit stream [1, 1, 0, 1, 1, 0, 1, 1] was segmented into dibits, with each pair mapped to quadrature phases (0°, 90°, 180°, 270°) using Gray encoding. A sampling frequency of 1000 Hz was utilized, with symbol durations set to Tb=1 for BPSK and Ts=2Tb​ for QPSK.
The modulated signals were visualized through three-panel subplots. In BPSK, abrupt 180° phase reversals were observed at bit boundaries, while QPSK exhibited four distinct phase states with 90° transitions every Ts​ seconds. The superior bandwidth efficiency of QPSK was confirmed, as it transmitted two bits per symbol within the same spectral occupancy required by BPSK for one bit. However, QPSK’s reduced phase separation (90° vs. BPSK’s 180°) was noted to increase vulnerability to phase noise and synchronization errors. Phase discontinuities at symbol boundaries were evident in both schemes, potentially leading to spectral regrowth in practical systems. The alignment of input bits with modulated signals was achieved using repelem() (BPSK) and index-based concatenation (QPSK).
The simulations operated under idealized conditions—no channel impairments (e.g., AWGN, multipath fading) were modeled, and critical aspects like carrier recovery and phase ambiguity resolution were omitted. Despite these limitations, the generated waveforms successfully demonstrated core principles of digital phase modulation, illustrating inherent trade-offs between spectral efficiency, error resilience, and implementation complexity.